Cameras

NavCam:

The Navigation Camera (Navcam) is a mast-mounted stereo pair of engineering cameras at 42.4 cm
baseline separation with a spectral bandpass at approximately 275 nm (passing longer wavelengths).
It will primarily be used for navigation purposes and general site characterization (360° panoramic
images and targeted images of interest, including terrain not viewable by the Hazcams).

Table of nav cam cahracteristics

Mastam:

Mastcam-Z is comprised of a pair of color-capable zoomable, focusable stereo cameras (“eyes”)
mounted on the rover’s Remote Sensing Mast (RSM). Each camera has identical zoom/focus
capabilities and a different set of spectral filters. The CCDs consists of 1648 x 1200 pixels, where
1600 x 1200 are photoactive pixels. These cameras are capable of video. They acquire color via
Bayer-pattern filters on the CCD, but also have selectable filters for science/geology applications.
For more details on how the Bayer pattern interacts with filters,

Tables for the characteristics of the cameras

Each Mastcam-Z camera has an 8-position filter wheel (Table 2-8). One of the positions per camera
is a broadband filter for use with the RGB Bayer color capability of the CCD. Six of the remaining
positions per camera provide color imaging capability in eleven unique wavelengths from 400 to
1000 nm. One additional filter per camera has a neutral density coating to provide direct solar
imaging capability in RGB (left eye) and 880 nm (right eye). The remaining six narrow-band filters
are used for science multispectral imaging.
Mastcam-Z multispectral, stereo, and panoramic images will use the RGB and narrow-band filters to
provide detailed geologic and geographic information. These images will explore the morphology,

topography, and geologic context along the rover's traverse in addition to constraining mineralogic,
photometric, and physical properties of the surface. The images will target places exhibiting color
variations, diagnostic morphologies, and potentially diverse chemistries and lithologies. These
images will monitor and characterize atmospheric and astronomical occurrences. In addition,
Mastcam-Z images will provide context and key engineering information in support of the sample
location, extraction, and caching, as well as documentation for driving, arm placement, and other
rover operations decisions

Methods

Calibrated vs Uncalibrated:

Mention the calibrated and the uncalibrated pipeline:

Implementation

OpenCv

Matlab

Metashape

pipeline form metashape

working

Intrinsics